## Slide 1: 資訊工程專題報告 Reliable In-Network Aggregation
109611058 王敬智
109611066 吳典謀
指導教授：林靖茹教授

## Slide 2: Reliable In-Network Aggregation
Aggregation
  Grouping and summarizing specific data
  Maybe a ML checkpoints or else
In-Network
  Aggregating in Network stage
  Not in host terminal
Reliable
  Packet loss handling
  Sequence ensure
  Acknowledgement
2
1
1

## Slide 3: Building concepts
In-Network – P4
  Software-Defined Network
  Programmable switch
  Can handling headers from layer 2 to layer 5
Reliability – TCP protocol
  Sequence is ensure
  Packet loss handling
  Packet Acknowledgement

## Slide 4: A multi-host In-Network aggregator
Receiving data from multiple hosts
Send to Receiver after aggregation
Works under TCP connections

## Slide 5: Topology
Environments
  Ubuntu: 20.04
  Mininet: 2.3.1b4
  bmv2
  p4c: 1.2.4.2
Devices
  4 Sender host
  1 Receiver host
  1 Aggregator switch
Connections
  4 TCP connections

## Slide 6: TCP Cheater- PSH
Storage initial TCP header of each host
  Store in register
  To calculate the relative sequence number
Intercept packet and Collect data
  Waiting for aggregate
Send the aggregated packet
  Modify to leader’s header
  Act as only one leader is sending
Recalculated checksum
  Packet is drop once error checksum
Aggregated
Packet
Original
Packet

## Slide 7: TCP Cheater- ACK
Replicated the ACK packet
  To cheat other host their packet is ACKed
  Using multicasting group
Modify the packet header
  Read the value from register
  Recover to original host header
Recalculated checksum
  Packet is drop once error checksum

## Slide 8: Ring Buffer
The buffer is in the following format:
  Sequence Number: The sequence number of corresponding payload.
  Payload: The aggregating result.
  Count: Record which host has aggregated in bit format.
Sequence Number | Payload | Count
1 | 4 | 0b1111
2 | 6 | 0b0111
3 | 6 | 0b0011
4 | 4 | 0b0001
5 | 0 | 0b0000

## Slide 9: Ring Buffer
There are min_index and max_index to maintain the buffer:
  If less than min_index: Drop (acked).
  If between min_index and max_index: Aggregate.
  If more than max_index: Check whether there is space, then save the payload.
Sequence Number | Payload | Count
1 | 4 | 0b1111
2 | 6 | 0b0111
3 | 6 | 0b0011
4 | 4 | 0b0001
5 | 0 | 0b0000
Min_index
Max_index

## Slide 10: Experiment Scenario
Sufficient bandwidth
Single slower sender
Slower receiver
All different bandwidth

## Slide 11: Scenario 1: Sufficient Bandwidth
All 1.0

## Slide 12: Scenario 2: Single Slower Sender
H1:0.2
H2:0.4
H3:0.6
H4:0.8

## Slide 13: Scenario 3: Slower Receiver

## Slide 14: Scenario 4: All different bandwidth
H1:0.2
H2:0.4
H3:0.6
H4:0.8

## Slide 15: Thank you for listening.
QA time